## Slide 1
Introduction to Tronix
NIT ConclaveX – Genesis ‘22
By, Robotics and Machine Intelligence (RMI)

## Slide 2: Electronic Components
An electronic component is any basic discrete device or physical entity in an electronic system used to affect electrons or their associated fields.
Electronic Components
As the name suggests, converts electric input to mechanical output or vice versa
Can only receive energy, which it can absorb, dissipate, or store it in an electric or magnetic field
Supplies energy to a circuit, or has the ability to electrically control the flow of electrons
Active
Components
Passive Components
Electromechanical Components
All electronic components have terminals which aid in connecting them with other components to form an electric circuit.
Notes: References:
https://www.electrical4u.com/active-and-passive-elements-of-electrical-circuit/
https://www.eletimes.com/what-are-electronic-components-types-classification-and-major-applications-of-electronic-components

## Slide 3: Resistor
A resistor is a passive electronic component that provides resistance in an electric circuit.
It is generally used to reduce current flow and divide voltages in circuits.
Resistors
Fixed Resistors
Have fixed resistance
Variable Resistors
Resistance can be varied
Rheostat
Potentiometer
Photoresistor
Notes: Fixed resistors are generally called simply as resistors
Under classifications, briefly mention about the colour codes in resistor and about the online calculators like this one - https://www.digikey.in/en/resources/conversion-calculators/conversion-calculator-resistor-color-code. Brief explanation will be given for rheostat and photoresistor. Potentiometer will be explained in the next slide.

## Slide 4: Potentiometer
A potentiometer is a three-terminal resistor with a sliding or rotating component that forms an adjustable voltage divider.
A potentiometer can be used as a rheostat if only two terminals are connected – either one of the end terminals (A or C) and the wiper terminal (B).
Notes: Potentiometers can provide highly precise sensing and measurement for linear or rotary movement as their output voltage is proportional to the wipers position

## Slide 5: Capacitor
Capacitor is a passive two-terminal electronic component that stores electrical energy in an electric field.
It consists of one or more pairs of conductors separated by insulating materials.
It is generally used for storing or releasing large amounts of energy in a short span of time, smoothening signals as in rectifiers, etc.
Fixed Capacitor
(Non-polarized)
Polarized Capacitor
Variable Capacitor

## Slide 6: Switches
Pushbutton Switch (Two Terminals)
Make Type
Break Type
Pushbutton Switch (Four Terminals)

## Slide 7
Switches
Slide Switch (Single-pole Double-throw)
Single-pole Single-throw

## Slide 8: Diode
Diode is a two-terminal semiconductor component that conducts current primarily in one direction; it has low resistance in one direction and high resistance in the other.
One of its applications is in rectifiers, wherein alternating current (AC) is rectified to direct current (DC).

## Slide 9: Light Emitting Diode (LED)
A Light Emitting Diode (LED) is a semiconductor light source that emits light when current flows through it.

## Slide 10: n-Segment Displays
7 Segment Display
9 Segment Display
14 Segment Display
16 Segment Display
Source: https://lastminuteengineers.com/seven-segment-arduino-tutorial/
Notes: Tell, n-segment displays are just like common anode or common cathode RGB LEDs.

## Slide 11: Bipolar Junction Transistor (BJT)
A Bipolar Junction Transistor (BJT) is a three-terminal semiconductor device in which the current flow between the collector and the emitter is controlled by the amount of current that flows through the base.
It is generally used as a switch or an amplifier.
Adjoining circuit diagrams show how NPN and PNP transistors can be used as a switch.
Did you know? There are billions of transistors in the processors powering the computers or mobile phones you are using for this workshop.
Source: https://learn.sparkfun.com/tutorials/transistors/applications-i-switches

## Slide 12: Power Supply
Most of the electric circuits that we deal with work on direct current (DC).
AC adapters and batteries are common DC power sources.
AC adapters convert AC to DC of required voltage using transformers, rectifiers, and power converters.
The laptop and mobile chargers are some common examples of AC adapters.
Batteries, on the other hand, provide DC supply by converting stored chemical energy to electric energy.
Batteries come in different types and sizes, usage of which depend on the power requirement of the device that is to be powered.
AC adapter with barrel pin connector (top left), AC adapter with USB type-C pin (bottom left), table top DC supply station (right)
From left to right: a large 4.5-volt 3R12 battery, a D Cell, a C cell, an AA cell, an AAA cell, an AAAA cell, an A23 battery, a 9-volt PP3 battery, and a pair of button cells (CR2032 and LR44)

## Slide 13: Batteries
AA Battery
100 – 500 mA
1200 – 2400 mAh
AAA Battery
50 – 200 mA
1000 mAh
9V Battery
500 – 800 mA
900 mAh
Lithium Ion Battery
(18650)
2 – 4 A
2000 – 4400 mAh
Lithium Polymer Battery
(18650)
>10 A
2000 – 6000 mAh
Lead Acid Battery
Notes: ### Have to mention the specifications of lead acid battery

## Slide 14: Batteries
C-Rating:
Usually the maximum discharge current rating is given in C-rating. The max current that can be drawn is = C-rating x capacity of battery
Example - a battery rated 2200 mAh 1C can produce a maximum discharge current of 2.2 A. [Always discharge max of 80 – 90% of maximum discharge current rating of battery]

## Slide 15: Batteries
Voltage Discharge Curve:
Another common misconception is regarding voltage discharge curve of batteries, it is not a linear one.
Refer to the datasheet of battery for obtaining the voltage discharge curve.

## Slide 16: Voltage Regulator
A voltage regulator is a device that creates and maintains a fixed output voltage, irrespective of changes to the input voltage or load conditions.
LD33V IC (3.3 V)
L7805CV IC (5 V)
L7812CV IC (12 V)

## Slide 17: Breadboard

## Slide 18: Breadboard
Series Connection
Parallel Connection

## Slide 19: Breadboards… :/
Notes: As you move on to make more complex circuits, or plan to convert the prototype of a circuit made in a breadboard to a robot which is in a vibrating environment, it becomes very clear that breadboards aren’t the best option and can be quite troublesome due to the dangling jumper wires. Here, comes PCBs, which we will discuss on the next slide.

## Slide 20: Perf Boards
Perf boards are used to assemble prototype boards where components are soldered on the board to obtain the required circuit. The connections are manually made using solder.

## Slide 21: Printed Circuit Boards (PCB)
Notes: Printed circuit boards have the copper traces and holes/pads for components as per PCB design, made specifically for the required circuit.

## Slide 22: Some Tips
Internet is your biggest resource. As far as electronics is considered, your doubts are a Google search away. Knowing how to Google is an important skill for self-learning.
Datasheet is the ultimate document to fetch technical details of any component. Most companies make it well-detailed and structured. You get most of the information required from the datasheet of the component and these are free to download. You can find lot of explanations of a component with facts direct from its datasheet. So, ability to read datasheets is a top-skill.
Experiment a lot. Sometimes when you get stuck with an issue, experimenting with it leads to more brilliant results and in-depth learning.
At start, most topics will be far apart and independent. But going further, you will realize all are twined in the same ball of wool.